## Slide 1: Three Stage Rocket Simulation
Dr. Peter H Zipfel,
Mastech.zipfel@cox.net
ROCKET6
Modeling and Simulation Technology Copyright 2013

## Slide 2: Features of ROCKET6 Simulation
Rocket
  Three-stage booster
    Sizing, propulsion, mass properties (AFRL/RZ)
    Aerodynamics from Missile DATCOM (AFRL/RW)
  Control
    Thrust Vector Control (TVC)
    Reaction Control System (RCS)
  Autopilot
    Acceleration in pitch and yaw
  Guidance
    Minimum fuel to insertion using linear tangent guidance law
  Navigation
    GPS and star tracker updating INS
Framework
  Dynamics
    6 Degrees of freedom
    WGS84 Earth model
  Simulation environment
    CADAC++
    Modular
    Multiple objects
    Monte Carlo
    Weather deck
    Plotting with CADAC Studio
  Platform
    Windows PC (32 or 64 bit)
    Microsoft Windows XP, Vista, 7)
    Microsoft C++ compilers

## Slide 3: ROCKET6 Input / Output
statn.asc
stat1.asc
stat2.asc
stat.asc
CADAC++ Frame
ROCKET6
.
.
.
plot1.asc
plotn.asc
plot2.asc
traj.asc
input.asc
plot.asc
tabout.asc
CADAC Studio

aero_deck_SLV.asc
weather_deck_Wallops.asc

## Slide 4: ROCKET6 Modular Architecture
kinematics( )
round6[100-149]
newton( )
round6[210-299]
euler( )
round6[150-199]
guidance( )
hyper[400-499]
control( )
hyper[500-599]
aerodynamics( )
hyper[100-199]
environment( )
round6[50-99]
startrack( )
hyper[800-849]
gps( )
hyper[700-799]
ins( )
hyper[300-349]
tvc( )
hyper[900-949]
rcs( )
hyper[50-99]
propulsion( )
hyper[10-49]
intercept( )
hyper[650-699]
forces( )
round6[200-209]












 Click for details

## Slide 5: Ascent Boost Phase
Guidance
Minimum fuel
Terminal conditions
Control
RCS lift-off
TVC endo
RCS exo
Navigation
GPS/INS
Vandenberg
CAV Insertion




I
II

## Slide 6: Generic Small Launch Vehicle
STAGE # |  | I | II | II
Thrust (vac) | N | 1,407,610 | 527,903 | 124,907
Isp (vac) | sec | 279.200 | 284.600 | 284.488
Exit Area | m^2 | 1.0601 | 0.5838 | 0.2318
STAGE # MODE | I | II | III
0 | F | F | F
1 | E | F | F
2 | D | F | F
3 | D | E | F
4 | D | D | F
5 | D | D | E
MODE |  | 0 | 1 | 2 | 3 | 4 | 5
Mass | kg | 48,983.70 | 17,802.18 | 15,490.50 | 5,935.89 | 5,024.48 | 1,732.35
CgX | m | 10.5265 | 6.7604 | 5.9100 | 4.1669 | 3.6510 | 2.8468
CgY | m | -0.0001 | -0.0002 | -0.0002 | -0.0005 | -0.0006 | -0.0017
CgZ | m | 0.0000 | -0.0001 | -0.0001 | -0.0002 | -0.0002 | -0.0006
Ixx | kg*m^2 | 21,943.38 | 6,952.22 | 5,043.47 | 2,046.77 | 1,519.04 | 486.49
Iyy | kg*m^2 | 671,626.02 | 158,830.26 | 51,912.18 | 15,531.49 | 5,157.65 | 2,373.15
Izz | kg*m^2 | 671,624.75 | 158,828.99 | 51,928.57 | 15,547.88 | 5,178.28 | 2,393.77
F – Fueled
E – Empty
D – Discarded
16.84 m
2.032 m
I
II
III
MASS PROPERTIES
PROPULSION
CONFIGURATION
MODE = Flight Phase
STAGE # = Configuration (F= Fueled, E=Empty, D=Discarded

## Slide 7: Insertion Trajectory
SIMULATION OUTPUT (typical)


I
II

Insertion
DESIRED INSERTION CONDITIONS
Distance from Earth center 6,481,000 m
Inertial velocity 6600 m/s
Flight path angle 1.5 deg
*** Boost engine cut-off time = 182.455 sec ***
Orbital position dbi = 6.481e+006 m Inertial speed dvbi = 6600.05 m/s Flight path angle thtvdx = 1.43257 deg
Position error ddb = -0.148621 m Speed error dvdb = -0.0523475 m/s Angle error thtvddbx = 0.0674341 deg

## Slide 8: Booster Flight Phases
Ascent Guidance
Insertion


I
II

Pitch Program
Ascent Guidance
Gamma Control
Dynamic pressure
Altitude
Inertial speed
Angle of attack
Sideslip angle
Flight path angle

## Slide 9: Thrust and Weight Balance
Insertion


I
II


## Slide 10: Aerodynamic Stability Characteristics


I
II

Insertion
Mostly statically unstable
stable
stable
un-stable

## Slide 11: TVC and RCS Control


I
II

Insertion
RCS
RCS
TVC
TVC
Max deflection 10 deg
Bandwidth 100 rad/sec
RCS
Roll moment 100 Nm
Pitch/Yaw moment 200,000 Nm
Dead zone 0.4 deg
Hysteresis 0.1 deg
TVC
RCS

## Slide 12: Booster Autopilot Phases
I
II

Insertion
Acceleration
Thrust Vector Pointing
Gamma
Vector Pointing
Acceleration Controller

## Slide 13: ROCKET6 Module Documentation
Geocentric and Geodetic Coordinate Systems
Integrating the Direction Cosine Matrix
Translational Equations of Motion
Newton Module
Attitude Equations of Motion
U.S. Standard Atmosphere 76
Turbulence
Dryden’s Turbulence Model
RCS Attitude Control
Schmitt Trigger
Roll Controller
Ascent Guidance for the 3 Stage Booster
Linear Tangent Guidance for Insertion
Flight-Plane Base Triad
Implementation of the LTG Controller
Program Flow
Time-to-Go Calculations
Motor Input Worksheet
Ascent Trajectory Planning
Inertial Navigation System
Space Stabilized Inertial Navigation System
Instrument Errors
NAVSTAR Global Positioning System (GPS)
GPS Satellite Position
GPS Satellite Constellation
The GPS Navigation Problem
Linearization of GPS Navigation Equation
Geometric Dilution of Precision Calculations
GPS User Measurements
Star Tracking and INS Update Procedure
Picking the Best Three Stars
Detector Principle of Operation
Modeling of Line-of-sight Measurements
Computing Tilt Updates for the INS
Wake Flow Model

## Slide 14: Geocentric and Geodetic Coordinate Systems
Geocentric coordinate system
1G axis points to the north pole
3G axis point to the center of the Earth
Transformation matrix of geodetic wrt geocentric coordinates

Geodetic coordinate system
1D axis points to the north pole
3D axis is normal to the local tangent plane and pointing down
lc geocentric latitude
ld geodetic latitude
d =ld - lc deflection angle
Kinematics

## Slide 15: Integrating the Direction Cosine Matrix
Fundamental problem in kinematics: Given the missile body rates in body coordinates
calculate the direction cosine matrix
– Compare the Euler transformation
– with the definition of the rotational time derivative
– and obtain
, relating the TM and the body rates
Direct solution by integrating the direction cosine matrix
– solve for
Initialization of TM
– Given the initial geodetic Euler angles y, q, f and the geodetic coordinates l, ld , h
[T]DI = cad_tdi84(l, ld, h)

Kinematics


## Slide 16: Translational Equations of Motion
Newton’s Second Law The rate of change of linear momentum equals the impressed force and is in the direction in which the force acts
– Assumptions (1) Speed well below the speed of light and (2) mass does not exceed that of natural substances
– The inertial frame I serves as reference frame and the center of mass B as reference point
– Rigid body assumption: mass is constant or only slowly varying so that
mass of vehicle
velocity of vehicle c.m. B wrt inertial frame I
aerodynamics and propulsive forces
weight
angular momentum
rotational time derivative wrt inertial frame I
– Translational equations of motion
– Acceleration is expressed in inertial coordinates ]I, the aerodynamic and propulsive forces in body coordinates ]B, and gravity in geocentric coordinates ]G
– Integration yields inertial displacement vector of vehicle c.m. B wrt center of the Earth I
♣
Newton

## Slide 17: Newton Module
– Functions starting with cad or mat are CADAC++ utilities
♣
Newton


## Slide 18: Attitude Equations of Motion
Euler
Euler’s Law:
angular momentum of vehicle B wrt to inertial frame I referred to vehicle c.m. B
moment of inertia of vehicle B referred to vehicle c.m. B
aerodynamic and propulsive moments referred to vehicle c.m. B
angular velocity of vehicle frame B wrt inertial frame I
Use Euler’s transformation to transfer the rotational derivative to the vehicle frame B
Introduce vehicle coordinates B
In component form
Solving for the state derivatives

Solving for the state derivatives



## Slide 19: Options of the Environment Module
Environment
mair=|matmo|mturb|mwind|
matmo = 0 US 1976 Standard Atmosphere (public domain shareware)
= 1 US 1976 Standard Atmosphere with extension up to 1000 km (NASA)
= 2 tabular atmosphere
mturb = 0 no turbulence
= 1 dryden turbulence model
mwind = 0 no wind
= 1 constant wind, input: dvaeg,psiwdx
= 2 tabular wind

## Slide 20: U.S. Standard Atmosphere 76
For dynamic pressure, Mach number, and aerodynamic heating calculations
Troposphere
Tropopause
Stratosphere
gK
Temperature
Density

Environment

## Slide 21: Turbulence
– Aircraft with velocity V encounters an air gust of length L
Vertical gust of simple sinusoidal form
– Aircraft traverses the gust in time
– Temporal frequency
– Gust velocity t in load-factor plane expressed in load-factor plane coordinates ]A
– Steady wind velocity (steady air mass A’ relative to Earth E in geographic coordinates ]G
– Velocity of vehicle B wrt Earth E
Total aircraft velocity wrt air mass A
Load-factor plane
– Velocity of vehicle B wrt turbulent air mass A in body coordinates
– is used to calculate the angle of attack a and sideslip angle b
♣
Environment

## Slide 22: Dryden’s Turbulence Model
Filter in the Laplace plane
Converting power spectral density function into a filter driven by white Gaussian noise s
– The output of the filter t is the turbulence velocity in the load-factor plane
Filter in the state space
Dryden filter in operation
♣

Environment

## Slide 23: ROCKET6 Aerodynamic Model

Aerodynamics
V vehicle velocity
M Mach number
q’ body rate in maneuver plane
d reference length
a‘ total angle of attack
thr base drag correction
Coefficients in aeroballistics coordinates (maneuver plane)
Note: roll damping is neglected

## Slide 24: Booster Thrust Vector Control
tvc

nozzle deflection angles
propulsion moment arm
c.m. location
thrust vector
Transformation sequence nozzle wrt body coordinates
TVC forces and moments in body coordinates
Pitch channel of TVC actuation (yaw channel similar)
♣
TVC and RCS Control

## Slide 25: Options of the RCS Module
RCS
mrcs_moment = |rcs_type||rcs_mode|
rcs_type = 0 no RCS thrusting
1 proportional moment thrusters
2 on-off moment thrusters (Schmitt trigger)
rcs_mode = 0 roll control only
1 all geodetic Euler angle control
2 thrust vector direction and roll angle control
3 incidence and roll angle control
mrcs_force = 0 no side force control
1 proportional side thrusters
2 on-off side thrusters (Schmitt trigger)
TVC and RCS Control

## Slide 26: RCS Attitude Control
The centerline 1B of the rocket is controlled by yaw and pitch angle commands, referred to geodetic north and local horizon (similar for roll angle, angle of attack and sideslip angle)
♣
RCS
Booster Autopilot

## Slide 27: Schmitt Trigger
16 reaction jets are required for independent three axis moment control
– Schmitt trigger is used to activate the control thrusters
Hysteresis h – rad
Mean dead zone D - rad
Slope of switching line t - sec
– Limit cycle period Tlc and amplitude Alc
M Moment – Nm
I MOI – kg m2
♣
RCS


## Slide 28: Acceleration Controller
Control
Acceleration autopilots provide fastest response and minimize miss distance
State variable model of missile pitch dynamics
Proportional/Integral control yields the best response using pole placement with
closed loop wn, z as input (in addition GP and a closed loop real pole must be chosen)

Booster Autopilot


## Slide 29: Ascent Guidance for the 3 Stage Booster
Guidance
For up to three stages of rocket propulsion
Constant thrust in each stage
Patterned after Saturn and Space Shuttle ascent guidance
Approach
  Selecting Linear Tangent Guidance (LTG) for thrust control
  Using LTG in the trajectory equations to fly towards a desired end-state
  Integrating the trajectory equations in closed form
  Computing on-line the required thrust vector direction
  Aligning the vehicle’s thrust axis in the required direction ♣
Booster Flight Phases

## Slide 30: Linear Tangent Guidance for Insertion
Guidance
Bryson’s finding: To minimize the time to intercept, the tangent of the thrust angle has to change linearly in time
  Assumptions
    Flat Earth, constant gravity, constant thrust, no aerodynamics
thrust angle
c constant
t thrust vector
B current vehicle position
D desired end state
– Thrust angle
– Thrust direction in vector form
.
ul unit vector in direction of velocity-to-go
tl reference time
D desired end state
l turning rate of thrust vector; normal to ul
♣
Bryson and Ho “Applied Optimal Control”, Hemisphere Publishing Co., 1975

## Slide 31: Flight-Plane Base Triad
Guidance
L launch
B current vehicle position
P predicted end-state
D desired end-state
I center of Earth
– Used to express the range-to-go and velocity to-be-gained vectors
The flight plane, defined by vectors
, is used to build the triad ud, uy, uz
– Calculation of base vectors
♣

## Slide 32: Implementation of the LTG Controller
Guidance
Based on the current vehicle state and the desired end-state, the commanded thrust vector direction is calculated, given the rocket motor performance
♣

## Slide 33: Program Flow
Guidance
The unit thrust vector command is calculated from time-to-go, range-to-go and the thrust integrals. A trajectory predictor-corrector cycle using Keplerian projections is added
♣

## Slide 34: Time-to-Go Calculations
Guidance
Evaluation of the thrust integrals depends on the accurate estimate of time-to-go
– Time-to-go tgo, from the current epoch to the end-state epoch, is determined based on the total burn time of the remaining stages
– The necessary burn time is obtained by integrating over the thrust profiles (acceleration) until the value equals the required end-state velocity vgo. The integration time is tgo
Updates are carried out for the residual burn time in the current stage and the BECO (Boost Engine Cut-Off) fractional burn time in the last stage
Characteristic time
(time of burn to zero mass)
mB vehicle mass - kg
mF total fuel in stage - kg
fp thrust - N
Isp specific impulse - sec
g0 gravity = 9.8066 - m/s2
Exhaust velocity
♣

## Slide 35: Motor Input Worksheet
Guidance
Stage n | vmass0 kg | fmass0 kg | exhaust_veln m/s | m kg/s | char _ timen s | event_time s | burnout_epochn s
1 |  |  |  |  |  |  | 
2 |  |  |  |  |  |  | 
3 |  |  |  |  |  |  | 
.
The rocket motor specs of the transfer vehicle are used in input.asc
– Select vmass0, fmass0, exhaust_vel and fuel flow dm/dt, then compute char_time, event_time and burnout_epoch for each stage
– For verification
Specific impulse
Thrust
♣

## Slide 36: Ascent Trajectory Planning
Guidance
Initial and end states have to be matched to the motor performance
Error messages of unreachable end-state
is a good indicator for
– The absolute value lamd of the turning rate vector
LTG performance
Initial saturation may lead to limit cycle and to large errors in meeting the desired orbital position
– LTG is based on several simplifying assumptions that are not met in 6 DoF WGS 84 simulations (real world). Therefore the parameters have to be carefully tuned
*** Warning: bad Kepler projection in 'guidance_ltg_pdct()' ***
The iteration in the ‘cadkepler( )’ function exceeded 20 counts. Usually due to bad conditioning of the beginning state; caused by bang-bang lamd and oscillatory tgo
The desired velocity-to-be-gained vgom becomes too great
*** Terminator: end-state cannot be reached ***
What to do if end-state is not reached
– Plot lamd and check whether it oscillates and/or saturates. If yes, do one or all of these:
Relax the desired end conditions
Extend the total impulse over longer time segments
Increase total impulse of rocket motors
♣
Booster Flight Phases


## Slide 37: Inertial Navigation System
INS
Principle of operation
– Gravitation is added to specific force
– Angular velocity is integrated to obtain transformation matrix
– Gyroscopes measure vehicle’s angular velocity
– Accelerometers measure vehicle’s specific force (aero. and prop.)
– Specific force (acceleration) is transformed to inertial coordinates
– Integration yields inertial velocity and position


## Slide 38: Space Stabilized Inertial Navigation System
INS
The output of the INS is
in computed inertial coordinates


## Slide 39: Instrument Errors
INS



## Slide 40: NAVSTAR Global Positioning System (GPS)
GPS
GPS consists of three segments
  Space Segment
    24 Space Vehicles (SV) in orbits at 26,560 km altitude
  Control Segment
    Ground station at Schriever AFB, Colorado, monitors and updates SVs
  User Segment
    GPS receiver in vehicle provides position, velocity and time
Principle of operation
  The receiver calculates its position by tracking a minimum of four SVs
    The range to an SV is determined from the measurement of the transit time of an RF signal traveling at the speed of light
    The position of the SV is sent to the user as ephemeris data
    Three SV measurements are needed to calculate the receiver’s position relative to the SVs
    The fourth measurement is used to correct the receiver clock errors
      The time measurement requires accurate time keeping at the SVs and the receiver. The receiver clock, being low-cost, has large errors ♣

## Slide 41: GPS Satellite Position
GPS
Periapsis = closest point to the Earth
u Argument of latitude (at SV epoch )
u = w + n
a Semi-major axis of elliptical orbit
e Eccentricity
i Inclination
W Longitude of the ascending node
w Argument of periapsis
n True anomaly
Orbital elements
SV
Locating the SV
W Longitude of the ascending node
i Inclination
w Argument of periapsis
n True anomaly
♣

## Slide 42: GPS Satellite Constellation
GPS
Arg. Lat. | A | B | C | D | E | F
1 | 59.06o | -129.34 | -104.27 | -81.82 | -16.52 | 22.91
2 | -52.21 | -41.66 | 158.43 | 53.91 |  | 134.24
3 | 156.34 | 94.07 | 124.59 | -178.51 | -145.19 | -108.71
4 | -171.07 | -9.32 | 29.11 | -44.18 | 120.66 | -80.42
5 |  | -149.14 |  | 139.12 | 76.04 | 151.48
6 |  |  |  | -114.22 |  | 
11
12
13
14
15
16
17
18
19
20
21
22
23
24
10
1
2
3
4
5
6
7
8
9
15
Slot #
♣

## Slide 43: The GPS Navigation Problem
GPS
Determine the user position and its clock bias, given the range measurements to four space vehicles
– User position from vector triangle
U User
I Earth center
Si i-th space vehicle
– User to SV distance obtained by scalar multiplication with unit vector
– Range measurement is corrupted by unknown user clock bias
c Speed of light
Tb User clock bias
– Substituting measurement equation into previous equation provides the solution
GPS navigation equation
– Calculating user position sUI and user clock bias Tb from four range measurements
and the accurately known satellite positions
– Non-linear equations!
♣

## Slide 44: Linearization of GPS Navigation Equation
GPS
Linearizing the navigation equations wrt the current user position
– Substituting into the navigation equation
– The underlined terms are the navigation equation at the neighboring position and are therefore satisfied identically.
– Introducing scalar perturbations
current value = neighboring value - increase
– Changing sign
yields the four linearized navigation equations
– For computations, the vectors are coordinated in inertial axes ]I
– Abbreviated as H x = z, the linearized navigation equation calculates the state x given the measurement z , with H as the measurement matrix
♣

## Slide 45: Geometric Dilution of Precision Calculations
GPS
Error propagation in GPS navigation
– Just as the neighboring user x is related to the change in measurements z
– Transformation of measurement errors into user position and timing errors (substitute (a) into (b) and with (c))
…so is its error d x related to the measurement errors d z
(a)
– The covariance matrix COV(…) is an expression of second order error statistics (E{…} is the expectation operator)
(b)
(c)
Dilution of precision
– The error transformation is governed by the H matrix, which expresses the geometric conversion from radial measurements to Cartesian coordinates
– Assume that all four measurements have the same error statistics, COV(z) = UNIT
– Geometric Dilution of Precision (GDOP) is the square root of the trace of COV(x)
To select the best satellite quadriga pick the four with minimum GDOP
♣

## Slide 46: GPS User Measurements
GPS
– Receiver noise and multi-path error modeled by 1st order Markov process
– Range bias error, initially drawn from Gaussian distribution, consists of
• Ephemeris error
• Uncompensated ionospheric delay
• Uncompensated tropospheric delay
– Delays are converted to m by the speed of light
All measurements and errors are expressed in m and m/s
– User clock bias error modeled by integral of Markov process between updates
Pseudo-range measurement
– Obtained from code tracking loop
True distance - m
DRi Range bias error – m
DNi Receiver noise and multi-path error – m
b User clock bias error - m
Delta-range measurement
– Obtained from carrier phase-lock tracking loop
True delta range – m/s
DNi Receiver dynamic noise error – m/s
f User clock frequency error – m/s
•
– Receiver dynamic modeled by 1st order Markov process
– User clock frequency error modeled by Markov process
♣

## Slide 47: GPS Kalman Filter
GPS
K.F.
Corrected Pos./Vel.
INS
Vehicle
Acceleration

-
+
-
Pseudo-R.
Receiver
SVs

+

Pos./Vel.
-
+
D Pos, D Vel
Prediction
– The GPS receiver pseudo-range and rate measurements
Tightly coupled
– The nonlinear K.F. operates on the difference between the receiver measurements and the INS derived predictions, converts them to position and velocity corrections and updates the INS
♣
Coupling of GPS and INS
  GPS and INS are complimentary
    GPS keeps low frequency errors small
    INS smoothes high frequency errors
  The Kalman filter bridges GPS and INS
    The K.F. filters the GPS measurements and updates the INS navigation solution
    Measurements: 4 pseudo-range and 4 pseudo-rate
    States: 3 positions, 3 velocities, user clock bias, user clock frequency
  The INS maintains the navigation solution during GPS outages
  The INS provides high data rate navigation data


## Slide 48: Star Tracking and INS Update Procedure
Star Tracker
Load the star catalog of the 25 brightest stars
  The LOS to the stars are given by their unit vectors in inertial coordinates
Determine the stars visible above horizon
  Above a given grazing angle
  Vehicle has to be high enough to see the stars
Get a fix of three stars that are spaced in an optimum pattern
  Use three star trackers onboard the vehicle
Measure each azimuth and elevation in the vehicle frame
Convert the LOS to inertial unit vectors using the INS
Compare the INS generated unit vectors with the catalog values
  The difference provides the tilt corrections for the INS ♣

## Slide 49: Picking the Best Three Stars
Determine those stars that are above a minimum angle of the local horizon
– The visible stars must be above the minimum elevation angle elmin
– Calculate the elevation angle el from the vehicle (computed) and star uSI unit vectors
From the visible stars find that triad that maximizes the volume of their parallelepiped
Number of possible triad combinations m
– Binomial coefficient
Example 12 visible stars
n = number of visible stars
q = 3 (triad)
♣
Star Tracker

## Slide 50: Detector Principle of Operation
Detector consists of two photo diodes, beam splitting mirror, watt meter, and a focusing objective
The starlight is focused by a lens onto the mirror
The mirror splits the beams equally onto two photo tubes
The photo tubes are wired in series with a watt meter
When the starlight is centered, both photo tubes generate the same current, and, wired with opposite polarity, the watt meter reads zero
Any off-zero reading of the watt meter is converted into a steering signal to turn the detector such as to zero the reading
Difficulty: photo tubes must have uniform sensitivity over time
Other schemes are used: Frequency scanning disk system (Whitford and Kron)
♣
Star Tracker

## Slide 51: Modeling of Line-of-sight Measurements
The true LOS of the triad are corrupted my measurement errors
– Calculate the true azimuth and elevation angles wrt the body frame
– Corrupt with bias and correlated noise all three star measurements
Typical measurement errors
– Bias error std. dev. = 0.1 mrad, drawn initially from a Gaussian distribution
– Noise std. Dev. = 0.05 mrad, 50Hz bandwidth, Gauss/Markov process
♣
Star Tracker

## Slide 52: Computing Tilt Updates for the INS
Convert az and el measurements to unit vectors in inertial coordinates
– Unit vector in body coordinates (do for every star)
– Use INS transformation matrix (with its tilt errors) to convert to inertial coordinates
Forming the tilt matrix
– The computed unit vectors are rotated through a small rotation tensor from the true unit vectors
– Because the rotation tensor executes small rotations
– Collecting the three vectors
– Solving for
– Tilt updates
♣

Star Tracker